## Slide 1: Virtual Environment Development
23rd Mar.

## Slide 2: DOE Ref. Bldg
Goal: Middle level
AHU | Number of terminals | Zone type
Bot level | 23 | 
Mid level | 21 | Active Storage (4), Conference room (2), Corridor (2), Dining (1), Enclosed Office (3), Lobby (1), Mechanical (1), Open Office (4), Restroom (1), Stair (2)
Top level | 22 | 

## Slide 3: Control variables
Variables to be controlled: 1 + 21*2 = 43
EnergyPlusToFMU has a constraint of 32 communication channel
 | Control variable | Node | Object in EnergyPlus
AHU | Supply air temperature | 149 | SetpointManager:Scheduled
Air terminal | Supply air temperature; Mass flow rate | 179, 182, 185, 188 … | AirTerminal:SingleDuct:UserDefined Actuator: Primary Air Connection - inlet mass flow rate Actuator: Primary Air Connection – outlet mass flow rate Actuator: Primary Air Connection – outlet temperature

## Slide 4: The problem
In Han’s simulation, we use coil:heating:electric for reheat
  No heating water plant and loop in Han’s simulation
Airterminal:singleduct:userdefined does not have the option of coil:heating:electric

## Slide 5: Solution 1
Use Airterminal:singleduct:userdefined to set the supply mass flow rate and supply air temperature
Add heating water loop and boiler
Pros
  More straightforward, benefit publication and open source the code
Cons
  More difficult to implement
    Redo Han’s simulation
  Other ways to generate the heating water loop and boiler?

## Slide 6: Solution 2
Use Airterminal:singleduct:uncontrolled to set the mass flow rate
Use equipment schedule to set the reheat
Pros
  Consistent to Han’s simulation
  Easy to implement
Cons
  Not straightforward